## Slide 1
MEMBER
Zama :B4
Experiment Group (EG)
Research Background
Distributed power supply has become widespread due to the adoption of smart grids.
In verification using simulation using a real machine, it is difficult to assume various situations.
Research Purpose
I want to simulate various situations using a generator.
A device that can easily be simulated doesn’t exist
Make equipment and build experiments
出典：横山明彦：スマートグリッド(電気新聞ブックス)

## Slide 2
IM-SG
INV
Controller
Arduino
Speed
Speed
LabVIEW
Speed
Voltage
Voltage Command
Speed Command
Turbine generator
AVR ・ GOV control system
Small-Scale Experiment system
Target image
The turbine type generator can be controlled by module using Arduino etc.
Scene of experiment
Excitation voltage

## Slide 3
～rpm
IM-SG set
IM
SG
Output to Controller
sensor
 | Stand Alone Mode ( only Arduino ) | External Mode ( with NI DAQ )
Normal operation | ✔ | ✔
High-performance operation | ✔ | ✔
Droop control |  | ✔
Virtual inertia |  | ✔
GOV & Excitor Model |  | ✔
Function
Production content
Speed
Voltage
Arduino
NI
DAQ
LabVIEW
Stand Alone Mode
External Mode
Speed
Voltage
Controller
Excitation Voltage to IM-SG
AVR
GOV
Target value command
Transistor circuit
voltage
IM-SG set
The rotational speed is measured using a magnetic sensor, and the measured rotational speed is output to the controller.
Controller
Command voltage and rotational speed from the controller. Also, by connecting to LabVIEW, the waveform etc. being measured are displayed.

## Slide 4
Create panel design of IM-SG set
Assembly of IM-SG set
Operation check of IM-SG set
Confirmation about GOV control
Operation check with inverter, IM-SG set and controller
Examination of AVR control
Step7
Step6
Step5
Step4
Step3
Step2
Step1
Internal production of IM-SG set
Purpose of research
Produce a small power generation unit that can simulate a power plant in laboratory.
Research plan
Construction of an experimental system simulating a small synchronous generator
Research theme